## Slide 1: CPU Temperature as a Device Biometric
Evan Smith
Department of Electrical Engineering and Computer Science
9/15/2021

## Slide 2: Overview
Goal: Use CPU temperature to classify devices
  MVP
    Classify by device chipset
    Authentication possible
  Stretch
    Classify by device
    Identification possible
Tasks
  Gather data
  Develop classifier
  Assess viability
Department of Electrical Engineering and Computer Science

## Slide 3: Background
Some potential use cases
  IoT verification
  Dual-factor authentication
Current identifiers
  IP Address – trivial to spoof
  MAC Address – “snoofable”, drivers available
  IMEI – possible to alter via flashing
Department of Electrical Engineering and Computer Science

## Slide 4: Experiment Design - Devices
Arduino Every (ATMega4809)
Arduino Uno (ATMega328P)
Department of Electrical Engineering and Computer Science
https://www.digikey.com/en/products/detail/arduino---bcmi-us-llc/ABX00028/10239971
https://www.robotshop.com/en/arduino-uno-rev3-smd.html?

## Slide 5: Data Gathering Process
Wrote C++ CPU soaking program
  Recorded 30 time series per device
  100 data points/series
Compiled labelled data
Normalized on initial temperature
Imported data to Jupyter Notebook
Department of Electrical Engineering and Computer Science

## Slide 6: Proving SVD Viability
Singular Value Decomposition (SVD)
  Extracts patterns from data and its relative importance
Department of Electrical Engineering and Computer Science

## Slide 7: Generating an Effective Classifier
Graph “fingerprints” of training data
  Inner product of training data and the first singular value vectors
Department of Electrical Engineering and Computer Science

## Slide 8: Quantifying The Classifier’s Success
Model training fingerprints as a gaussian
  Calculate each test fingerprint’s most likely device distribution
  Overall accuracy: 85%
Department of Electrical Engineering and Computer Science
Device ID | Classification Accuracy | 
 | 2 Singular Values | 3 Singular Values
1 | 90% | 90%
2 | 10% | 60%
3 | 100% | 100%
4 | 80% | 80%
Overall | 70% | 85%

## Slide 9: Conclusion – Device Biometrics Are Viable!
High accuracy of classifier promising
  Especially given data collection issues with hardware
    Multithreading
    Device application and form factor
Both authentication and identification possible
  Can achieve higher TP or lower FN depending on use case
Department of Electrical Engineering and Computer Science

## Slide 10: Future Work
Improving CPU soak program
  Task-based architecture
  Variable load parameter
Exploring additional biometrics
  Processing time
  Network card speed
Mimicking Viola-Jones pattern for higher granularity
Department of Electrical Engineering and Computer Science